## Slide 1: Computer Architecture Experiment
lab7
College of Computer Science & Engineering
Zhejiang University

## Slide 2: Topics
0、Basic knowledge
1、Function Units design
2、Single-cycle CPU design
3、Multiple-cycle CPU design
4、5-stage of pipelined CPU design
5、Pipelined CPU with stall
6、Pipelined CPU with forwarding
7、Pipelined CPU resolving control hazards
8、Pipelined CPU support execution 16 MIPS Instructions
9、Review

## Slide 3: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Precaution

## Slide 4: Experiment Purpose
Understand why and when Control Hazards arise
Master the methods of resolving Control Hazards
  Freeze or flush
  Predict-not-taken
  Predict-taken
  Delayed-branch
Master the methods of 1-cycle stall of Predict-not-taken and Predict-taken branch.
master methods of program verification of Pipelined CPU resolving control hazards

## Slide 5: Experiment Task
Improve the design of Datapath of 5-stages Pipelined CPU via reducing 3 control stall to 1 stall when using flush
  Bring forward calculation of condition & branch address
  Bring forward bypass unit
Verify the Pipeline CPU with program and observe the execution of program

## Slide 6: Control Hazard Definition
Control Hazards arise from the pipelining of branches and other instructions that change the PC.
Control hazards can cause a greater performance loss for our MIPS pipeline compared with data hazards.
Reducing Pipeline Branch Penalties.

## Slide 7: Instruction Demo

## Slide 8: Execution result

## Slide 9: Methods of resolving Control hazards
Freeze or flush the pipeline
Predict-not-taken
Predict-taken
Delayed branch

## Slide 10: Freeze method

## Slide 11: Predict-not-taken( not in lab)
How to implement it ?
Normally: pcpc+4, no stall whenever ((exop or memop )== branch)
If mem_op=branch and condition_code==1, then Kill the following 3 instructions flying in pipeline.

## Slide 12: Predict taken only when branch target can be got earlier that condition code
However there’s no advantage for MIPS pipeline, but if the datapath can be changed as following.
NOT in Lab too.

## Slide 13: Reduce the control stall by calculate target and cc asap.
Bring forward calculation of branch condition from MEM Stage to EX Stage, stall reduce from 3-cycle to 2-cycle.

## Slide 14: Reduce the control stall by calculate target and cc asap.
Then bring forward from EX to ID, stall reduce from 2-cycle to 1-cycle.
store
load

## Slide 15: What we have done by far

## Slide 16: The control logic
Stall
  Control stall: ex_op / mem_op is branch or jmp. (Flush)
  Load stall: (ex_op=lw) & ((ex_rd=id_rs) & exist_id_rs)
  or ((ex_rd= id_rt) & exist_id_rt )
FWA:
  1: (ex_op=ALUop) && ((ex_rd=id_rs) & exist_id_rs)
  2: (mem_op=ALUop/LWop) && ((mem_rd=id_rs) & exist_id_rs)
  0:
FWB:
  1: (ex_op=ALUop) && ((ex_rd=id_rt) & exist_id_rt)
  2: (mem_op=ALUop/LWop) && ((mem_rd=id_rt) & exist_id_rt)
  0:

## Slide 17: Datapath resolving Control Hazards

## Slide 18: Why Move the forwarding control logic to ID stage ?
alu r1, r2, R3
BNE r4,r1,L1
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Reg
Reg
CC &
Target is OK
What if CC and target is calculated in ID stage ?
alu r1, r2, R3
BNE r4,r1,L1
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Reg
Bubble
Reg
Before improvement

## Slide 19: Why Move the forwarding control logic to ID stage ?
alu r1, r2, R3
BNE r4,r1,L1
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Reg
Reg
CC &
Target is OK
Move the forwarding control logic into ID stage,
and Also, send out ALUoutput and LWDR earlier before the latch.
alu r1, r2, R3
BNE r4,r1,L1
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Reg
Bubble
Reg

## Slide 20: Move forward the forwarding control logic & send out ALUoutput/LWDR before the latch.

## Slide 21: But new stall still arise
So what about your stall logic and forwarding control logic ?
LW r1, 8(r2)
BNE r4,r1,L1
Reg
ALU
DMem
Ifetch
Reg
Ifetch
ALU
DMem
Reg
Bubble
Reg

## Slide 22: Precautions
1、According to datapath to modify the modules of top module, then modify the definitions of the modules.
2、The signals which transfer from former stage to later stage should be stored to stage registers temporally.
3、Bring forward Bypass Unit to ID Stage (3 selection sources: EXE.ALU, MEM.ALU, MEM.LW)
4、Bring forward Calculations of Condition and Branch Address to ID Stage.
5、JUMP Instruction. (After JUMP is A Stall)

## Slide 23: Observation Info
Input
  West Button: Step execute
  South Button: Reset
  4 Slide Button: Register Index
Output
  0-7 Character of First line: Instruction Code
  8 of First line : Space
  9-10 of First line : Clock Count
  11 of First line : Space
  12-15 of First line : Register Content
  Second line : “stage name”/number/type
  stage name: 1-”f”, 2-”d”, 3-”e”, 4-”m”, 5-”w”

## Slide 24: Program for verification
 | Instruction | Bin Code | Address | Inst. Type
 | lw r1, $20(r0) | 0x8c01_0014 | 0 | 6
 | lw r2, $21(r0) | 0x8c02_0015 | 1 | 6
 | add r3, r1, r2 | 0x0022_1820 | 2 | 1
 | add r2,r0,r0 | 0x0000_1020 | 3 | 1
 | sub r4, r1, r3 | 0x0023_2022 | 4 | 2
 | and r5, r3, r4 | 0x0064_2824 | 5 | 3
 | or r7, r5, r7 | 0x00a7_3825 | 6 | 4
 | beq r5,r7,-6 | 0x10a7_fffa | 7 | 8
 | add r7,r0,r1 | 0x0001_3820 | 8 | 1
 | jmp 0 | 0x0800_0000 | 9 | 9
 | Add r7, r0, r0 | 自己编码 | A | 1

## Slide 25
Thanks!