## Slide 1: Computer Architecture Experiment 5－Memory Hierarchy
Jiang Xiaohong

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Precaution
Checkpoints

## Slide 3: Experiment Purpose
Understanding the principle of Memory Hierarchy
Implement CPU with cache and memory by two steps
  Implement a CPU accessing memory in multiple cycle Implement a CPU with cache – memory two level hierarchy

## Slide 4: Part I CPU access Mem in multiple cycles
Understand the principle of CPU accessing Mem. in multiple cycles.
Master the design methods of pipelined CPU accessing Mem. in multiple cycle.
master methods of program verification of Pipelined CPU accessing Mem. in multiple cycle.

## Slide 5: Experiment Task
Design of Pipelined CPU accessing Mem. in multiple cycle
  Redesign Inst. ROM & Data RAM
  Modify CPU Controller
  Modify datapath
Verify the Pipelined CPU with program and observe the execution of program

## Slide 6: Inst. ROM’s Job
Initial State: S_IDLE
Working State: S_READ
Read for 8 cycles, then output the value, set the signal ACK
STALL = CS & ~ACK

## Slide 7: Data RAM’s Job
Initial State: S_IDLE
Working State: S_READ/S_WRITE (according to signal we)
Read/Write for 8 cycles, then output the value/write the value, set the signal ACK
STALL = CS & ~ACK

## Slide 8: When ROM&RAM STALL
Inst. ROM Stalls, Stall should be in ID stage otherwise jump indicator would be lost
  if_en=0, id_en=0, rst_exe=1
DATA RAM stalls
  …, rst_wb=1

## Slide 9: Add TCR in CP0
TCR - Tick Counter Register
TCR ++ when System Clock
Cycle goes on
// CP0 registers
localparam
//CP0_SR = 0,
//CP0_EAR = 1,
CP0_EPCR = 2,
CP0_EHBR = 3,
//CP0_IER = 4,
//CP0_ICR = 5,
//CP0_PDBR = 6,
//CP0_TIR = 7,
//CP0_WDR = 8,
CP0_TCR = 9;

## Slide 10: Datapath of CPU accessing Mem. in multiple cycle

## Slide 11: Code Example (1)
module inst_rom (
input wire clk,
input wire rst,
input wire cs,
input wire [31:0] addr,
output reg [31:0] dout,
output reg stall
);

## Slide 12: Code Example (2)
module data_ram (
input wire clk,
input wire rst,
input wire cs,
input wire we,
input wire [31:0] addr,
input wire [31:0] din,
output reg [31:0] dout,
output reg stall
);

## Slide 13: Instr. Mem.(1)
0: 3c010000 lui R1,0x0 //main entry
4: 24210040 addiu R1,R1,64
8: 40811800 mtc0 R1, R3
c: 00001020 add R2,R0,R0
10: 00001820 add R3,R0,R0
14: 40044800 mfc0 R4,R9
18: 00002820 add R5,R0,$0
1c: 20420001 addi R2,R2,1 //loop
20: 28412710 slti R1,R2,10000
24: 1420fffd bne $1,R0,-2 //jump to loop
28: 00000000 nop

## Slide 14: Instr. Mem.(2)
2c: 40054800 mfc0 R5, R9
30: 00a42822 sub R5, R5, R4
34: 20420001 addi R2,R2,1 //loop
38: 0800000d j 34
3c: 00000000 nop
40: 20630001 addi R3,R3,1 //handler
44: 42000018 eret
48: 00000000 nop

## Slide 15: Simulation (1)

## Slide 16: Simulation (2)

## Slide 17: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 18: Part II Cache design
Understand Cache Line.
Understand the principle of Cache Management Unit (CMU) and State Machine of CMU.
Master the design methods of CMU.
Master the design methods of Cache Line.
master verification methods of Cache Line.

## Slide 19: Experiment Task
Design of Cache Line and CMU.
Verify the Cache Line and CMU.
Observe the Waveform of Simulation.

## Slide 20: Cache Line

## Slide 21: Cache Mode
Direct Map
Write Back
Write Allocate

## Slide 22: Address
Bytes of word = 4, WORD_BYTES_WIDTH = 2
Words of line = 4, LINE_WORDS_WIDTH = 2
Tag bits = 22
Address bits = 32
LINE_INDEX_WIDTH = ADDR_BITS - TAG_BITS - LINE_WORDS_WIDTH - WORD_BYTES_WIDTH = ?
Line Number = 64
Notes: 6
2^6 = 32

## Slide 23: Cache Line Memory
reg [LINE_NUM-1:0] inner_valid = 0;
reg [LINE_NUM-1:0] inner_dirty = 0;
reg [TAG_BITS-1:0] inner_tag [0:LINE_NUM-1];
reg [WORD_BITS-1:0] inner_data [0:LINE_NUM*LINE_WORDS-1];

## Slide 24: Input and output Signals of Cache Line
module cache (
input wire clk, // clock
input wire rst, // reset
input wire [ADDR_BITS-1:0] addr, // address
input wire store, // set valid to 1 and reset dirty to 0
input wire edit, // set dirty to 1
input wire invalid, // reset valid to 0
input wire [WORD_BITS-1:0] din, // data write in
output wire hit, // hit or not
output reg [WORD_BITS-1:0] dout, // data read out
output reg valid, // valid bit
output reg dirty, // dirty bit
output reg [TAG_BITS-1:0] tag // tag bits
);

## Slide 25: Read and Write Cache
dout <= inner_data[addr[ADDR_BITS-TAG_BITS-1:WORD_BYTES_WIDTH]];
if (store || edit)
inner_data[addr[ADDR_BITS-TAG_BITS-1:WORD_BYTES_WIDTH]] <= din;

## Slide 26: Dirty, Valid, tag of Cache
invalid
inner_valid[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?
inner_dirty[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <= ?
load
inner_valid[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?
inner_dirty[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?
inner_tag[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?
edit
inner_dirty[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?
inner_tag[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]] <=?

## Slide 27: output of Dirty, Valid, tag, hit
valid <= inner_valid[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]]
dirty <= inner_dirty[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]]
tag <= inner_tag[addr[ADDR_BITS-TAG_BITS-1:LINE_WORDS_WIDTH+WORD_BYTES_WIDTH]]
hit = ?? & ??

## Slide 28: Simulation Example
#210 load = 1; din = 32'h11111111; addr = 32'h00000000;
#20 addr = 32'h00000004;
#20 addr = 32'h000000A8;
#20 addr = 32'h0000001C;
#20 load = 0; addr = 32'h000000B4; din = 0;
#100 edit = 1; din = 32'h22222222; addr = 32'h00000008;
#100 edit = 0; din = 0; addr = 0;
initial forever #10 clk = ~clk;

## Slide 29: Simulation Example

## Slide 30: Simulation Example

## Slide 31: Simulation
Write Simulation Code yourself
  cache initialization
  read
    miss
    hit
  write
    miss
    hit

## Slide 32: Cache Management Unit

## Slide 33: Cache Operation Flow
Read (Hit/Miss)
Write (Hit/Miss)
Replace (Clean/Dirty)

## Slide 34: Cache Management State Machine
S_IDLE
S_BACK
S_BACK_WAIT
S_FILL
S_FILL_WAIT
Read/Write Hit
Miss & Dirty
Writing Back
Reading Allocate
Miss & Clean
Notes: S_IDLE：空闲状态，不进行Memory操作。
S_BACK：将数据写回到Memory，由计数器控制直到整个Cache Line 全部写回。
S_BACK_WAIT：等待一个时钟，需要释放对Memory的片选以准备下次操作。
S_FILL：从Memory读取数据，由计数器控制直到整个Cache Line 全部读取完毕。
S_FILL_WAIT：等待一个时钟，保证最后一个数据成功写入Cache。

## Slide 35: State Machine
Next State Logic
State assignment
Output

## Slide 36: Next logic (1)
S_IDLE: begin
if (en_r || en_w) begin
if (cache_hit)
next_state = S_IDLE;
else if (cache_valid && cache_dirty)
next_state = S_Back;
else
next_state = S_FILL;
end
end
S_BACK: begin
if (mem_ack_i)
next_word_count = word_count + 1'h1;
else
next_word_count = word_count;
if (mem_ack_i && word_count == {LINE_WORDS_WIDTH{1'b1}})
next_state = ???;
else
next_state = ???;
end

## Slide 37: Next logic (2)
S_BACK_WAIT: begin
next_word_count = 0;
next_state = ???;
end
S_FILL: begin
if (mem_ack_i)
next_word_count = word_count + 1'h1;
else
next_word_count = word_count;
if (mem_ack_i && word_count == {LINE_WORDS_WIDTH{1'b1}})
next_state = ???;
else
next_state = ???;
end
S_FILL_WAIT: begin
next_word_count <= 0;
next_state <= ???;
end

## Slide 38: Perform State Assignment
always @(posedge clk) begin
if (rst) begin
state <= 0;
word_count <= 0;
end
else begin
state <= next_state;
word_count <= next_word_count;
end
end

## Slide 39: Output (1)
case (next_state)
S_IDLE: begin
cache_addr = addr_rw;
cache_edit = en_w;
cache_din = data_w;
end
S_BACK, S_BACK_WAIT: begin
cache_addr = {addr_rw[31:LINE_WORDS_WIDTH+2], next_word_count, 2'b00};
end
S_FILL, S_FILL_WAIT: begin
cache_addr = {addr_rw[31:LINE_WORDS_WIDTH+2], word_count_buf, 2'b00};
cache_din = mem_data_syn;
cache_store = mem_ack_syn;
end
endcase

## Slide 40: Output (2)
case (next_state)
S_IDLE, S_BACK_WAIT, S_FILL_WAIT: begin
mem_cs_o <= 0;
mem_we_o <= 0;
mem_addr_o <= 0;
end
S_BACK: begin
mem_cs_o <= 1;
mem_we_o <= 1;
mem_addr_o <= {cache_tag, addr_rw[31-TAG_BITS:LINE_WORDS_WIDTH+2], next_word_count, 2'b00};
end
S_FILL: begin
mem_cs_o <= 1;
mem_we_o <= 0;
mem_addr_o <= {addr_rw[31:LINE_WORDS_WIDTH+2], next_word_count, 2'b00};
end
endcase

## Slide 41: Simulation (1)
module inst (
input wire clk,
input wire rst,
input wire [3:0] index, // instruction index
output wire valid, // stop running if valid is 0
output wire write, // write enable signal for cache
output wire [31:0] addr // address for cache
);
reg [33:0] data [0:7];
initial begin // clock cycles are only for reference
data[0] = 34'h200000004; // read miss 1+17
data[1] = 34'h300000018; // write miss 1+17
data[2] = 34'h200000008; // read hit 1
data[3] = 34'h300000014; // write hit 1
data[4] = 34'h210000004; // read & clean replace 1+17
data[5] = 34'h310000018; // write & dirty replace 1+17*2
data[6] = 34'h310000008; // write hit 1
data[7] = 34'h0; // end total: 92
end
assign
valid = data[index][33],
write = data[index][32],
addr = data[index][31:0];
endmodule

## Slide 42: Simulation (2)
`timescale 1ns / 1ps
module top (
input wire clk,
input wire rst,
output reg [7:0] clk_count = 0,
output reg [7:0] inst_count = 0,
output reg [7:0] hit_count = 0
);
// instruction
reg [3:0] index = 0;
wire valid;
wire write;
wire [31:0] addr;
wire stall;
inst INST (
.clk(clk),
.rst(rst),
.index(index),
.valid(valid),
.write(write),
.addr(addr)
);
always @(posedge clk) begin
if (rst)
index <= 0;
else if (valid && ~stall)
index <= index + 1'h1;
end
// ram
wire mem_cs;
wire mem_we;
wire [31:0] mem_addr;
wire [31:0] mem_din;
wire [31:0] mem_dout;
wire mem_ack;
data_ram #(
.ADDR_WIDTH(5),
.CLK_DELAY(3)
) RAM (
.clk(clk),
.rst(rst),
.addr({26'b0, mem_addr[5:0]}),
.cs(mem_cs),
.we(mem_we),
.din(mem_din),
.dout(mem_dout),
.stall(),
.ack(mem_ack)
);

## Slide 43: Simulation (3)
// cache
cmu CMU (
.clk(clk),
.rst(rst),
.addr_rw(addr),
.en_r(~write),
.data_r(),
.en_w(write),
.data_w({16'h5678, clk_count, inst_count}),
.stall(stall),
.mem_cs_o(mem_cs),
.mem_we_o(mem_we),
.mem_addr_o(mem_addr),
.mem_data_i(mem_dout),
.mem_data_o(mem_din),
.mem_ack_i(mem_ack)
);
// counter
reg stall_prev;
always @(posedge clk) begin
if (rst)
stall_prev <= 0;
else
stall_prev <= stall;
end
always @(posedge clk) begin
if (rst) begin
clk_count <= 0; // 时钟计数
inst_count <= 0; // 指令计数
hit_count <= 0; // 命中计数
end
else if (valid) begin
clk_count <= clk_count + 1'h1;
inst_count <= index + 1'h1;
if (~stall_prev && ~stall)
hit_count <= hit_count + 1'h1;
end
end
endmodule

## Slide 44: Simulation (4)
module sim_top;
// Inputs
reg clk;
reg rst;
// Outputs
wire [7:0] clk_count;
wire [7:0] inst_count;
wire [7:0] hit_count;
// Instantiate the Unit Under Test (UUT)
top uut (
.clk(clk),
.rst(rst),
.clk_count(clk_count),
.inst_count(inst_count),
.hit_count(hit_count)
);
initial begin
// Initialize Inputs
clk = 0;
rst = 1;
// Wait 100 ns for global reset to finish
#95 rst = 0;
// Add stimulus here
end
initial forever #10 clk = ~clk;
endmodule

## Slide 45: Result (1)
Read miss at 0x00000004

## Slide 46: Result (2)
Write miss at 0x00000018
Read hit at 0x00000008
Write hit at 0x00000014

## Slide 47: Result (3)
Read & clean replace at 0x10000004

## Slide 48: Result (4)
Write & dirty replace at 0x10000018
Write hit at 0x10000008

## Slide 49: Performance Analysis
Miss Penalty
  When clean, MP = 17
  When dirty, MP = 34
Result
  CLK_COUNT = 92
  INST_COUNT = 7
  HIT_COUNT = 3

## Slide 50: Report
Including：
CP1:
  Waveform Simulation of Cache Line.
CP2:
Waveform Simulation of CMU.

## Slide 51: Checkpoint
Download FPGA board and test whether the pipeline can run with cache and memory correctly.
Give a signal to show whether cache is miss(light) or hit ?
Give a signal to show whether it’s a read or write ?